## Slide 1: Drilling Practices Casing Operations Handling, Running - Procedure Landing Casing, Slips, Seals
Notes: Forward-looking statements and estimates in these presentation materials are subject to risks and uncertainties which could cause actual results to differ materially. A discussion of significant risk factors can be found on page 40 of this booklet.

## Slide 2: Casing Joints
A casing string is composed of a number of segment lengths referred to as “joints”.
A “joint” of casing is identified by four parameters:
  Outside diameter (OD)
  Normal weight per foot
  Grade of steel
  Thread type of connection at either ends of the “joint”.

## Slide 3: Pipe Marking
Pipe should be marked by die stamp or with paint as follows:
  Manufacture’s / Processor’s name or mark
  API Spec 5CT: Size, Weight per foot, Grade
  Process of manufacture, length, test pressure, type of thread, heat treatment.

## Slide 4: Pipe Marking
Each joint should be color coded with a paint band encircling the pipe on or near the coupling or box.
Pipe and couplings may have an external coating for protection from rust while in transit.

## Slide 5: Pipe Grade Color Coding

## Slide 6: Receiving Pipe Tally

## Slide 7: Receiving Pipe Tally

## Slide 8: Casing Running and Landing
Preparation to run casing:
  Prior to running, perform landing calculations per weight and grades
  Clearly label all joints to be left OUT
  Review planned landing details with:
    Rig Personnel - Toolpusher, Driller
    Casing Crew - Supervisor

## Slide 9: Casing Running and Landing
Running casing:
  Consider - Re-tally and re-number as run in hole (Running Order)
  Run pipe at a moderate rate to minimize surge pressures created while lowering casing into wellbore ~1,000 fph or less per well conditions.

## Slide 10: Running Pipe Tally

## Slide 11: Running Pipe Tally

## Slide 12: Running Pipe Tally - Landing

## Slide 13: Casing Accessories

## Slide 14: Pipe Deck - Offshore

## Slide 15: Running Casing Onshore / Offshore

## Slide 16: Casing Handling Equipment
Side Door Elevator
Single Joint Elevator
Casing Drift
Safety Clamp
Spider Elevator
Spider Slip
Casing Slip
Stabbing Guide
Clamp On

## Slide 17: Casing Accessories - Protectors

## Slide 18: Casing Power Tong

## Slide 19: Elevator / Spider
Spider Elevator
Spider Slip

## Slide 20
Spider Elevator
Casing Elevator
Single Elevator

## Slide 21: Casing Connection Type  Casing Handling
Threaded and coupled;
Integral flush;
Integral upset connection
b and c  use Slip Type Elevator
a  use Side Door Elevator

## Slide 22: Casing Handling Equipment – CDS (Casing Drive System)

## Slide 23: Casing Dope

## Slide 24: Casing MU Torque Monitoring
Premium Thread
Torque Chart
Torque Turn Equipment

## Slide 25: Drilling Sequence Drive Pipe
Cut off excess Drive Pipe per program
Install temporary wellhead
Nipple up Diverter
Drill Conductor hole

## Slide 26: Drilling Sequence Structural (Conductor)
Run Conductor Pipe
Run conventional float equip (thread lock btm 2 jts)
Pump Cement to Surface - be prepared to washout excess cement
Center Conductor prior to cement set

## Slide 27: Drilling Sequence Structural (Conductor)
Wait on Cement
Cut Temporary Head off Drive pipe
Cut Conductor pipe in preparation for wellhead equipment

## Slide 28: Drilling Sequence Structural (Conductor)
Install “A” section of wellhead
Weld “A” section on Conductor
Nipple up Diverter
Drill Surface Hole

## Slide 29: Drilling Sequence Surface
Run Surface Pipe
Run conventional float equip (thread lock btm 2 jts)
Pump Cement to Surface - be prepared to washout excess cement

## Slide 30: Drilling Sequence Surface
Install Slips:
  If hand set, wait on cement before remove Diverter (pump time + [1-2] hrs, discuss with Supervisor)
  If drop slips, then make sure no collars are in the way, may have to remove riser above Diverter

## Slide 31: Drilling Sequence Surface
Remove Diverter if not done so already
Install “B” section packoff in preparation for next Wellhead section

## Slide 32: Drilling Sequence Surface
Ready for next Wellhead section

## Slide 33: Drilling Sequence Surface
Install “B” section
Test void section between “A” and “B” sections:
  Do not exceed 80% of burst for Conductor
  Do not exceed 80% of collapse for Surface
Install BOP’s
Drill Next Hole

## Slide 34: Drilling Sequence Next Hole (Int or Prod)
Install Casing Rams in BOP’s
Run Next Pipe
Run conventional float equip (thread lock btm 2 jts)
Pump Cement per program

## Slide 35: Drilling Sequence Next Hole (Int or Prod)
Install Slips:
  If hand set, wait on cement before remove BOP (pump time + [1-2] hrs, discuss with Supervisor)
  If drop slips, then make sure no collars are in the way, may have to remove riser above BOP’s

## Slide 36: Drilling Sequence Next Hole (Int or Prod)
Remove BOP’s if not done so already
Install “C” section packoff in preparation for next Wellhead section

## Slide 37: Drilling Sequence Next Hole (Int or Prod)
Ready for next Wellhead section

## Slide 38: Drilling Sequence Next Hole (Int or Prod)
Install “C” section
Test void section between “B” and “C” sections:
  Do not exceed 80% of burst for Surface Pipe
  Do not exceed 80% of collapse for Next Pipe, check loads
If more hole, install BOP’s
If not, install Tree

## Slide 39: Liner
Run Liner to depth, set Hanger
  Perform cement job
  Don’t over-displace, Liner wipers have tendency to be inefficient
Pump cement above hanger (discuss with Supervisor), unless planning on running a Liner top squeeze
Drill Pipe to run and cement Liner
Liner Hanger
Liner

## Slide 40: Liner
After pumping cement
  Immediately, pull 5-10 stands of DP to circulate clean
  Be prepared for the U-Tubing
  Upfront planning is required & critical
Tieback:
  If not using,then install Tree.
  If using, then another Wellhead section is required.
Drill Pipe TOH
Liner Hanger
Liner

## Slide 41: Ready for Completion